## Slide 1
Technical overview of single-cell transcriptomics methods.
1. General considerations / experimental settings.
2. scRNA-seq plates-based methods: template-switch versus T7.
3. Droplet-based scRNA-seq.
4. Combinatorial indexing approaches for scRNA-seq
5. Other –omics approaches.
6. Integrated multi-omics approaches.
Sébastien Smallwood – FMI
sebastien.smallwood@fmi.ch
SIB / SciLifeLab - Single-cell RNA-Seq Analysis (Leysin 2019)

## Slide 2
Technical overview of single-cell transcriptomics methods.
Svensson et al. Nat Protocols, 2018
Sébastien Smallwood – FMI
sebastien.smallwood@fmi.ch
SIB - Single-cell RNA-Seq Analysis (Leysin 2019)

## Slide 3
How to select the right protocol for a given biological question?
How many cells do I need to sequence?
Are my cells precious or can collection repeated easily?
How can I collect cells? How many cells can I collect in one experiment?
Available equipment / Cost considerations...
Plate-based approaches are still relevant in 2019.
Collecting healthy single cells is CRITICAL and can be challenging. Optimisations are required.
In 2019, success of scRNA-seq is more dependent on cells than actual protocol
Many methods, many “copies”
Common / specific issues…little extensive comparisons…
Differences between labs and projects / cell types: same method -> different quality datasets
Replicates are still needed.

## Slide 4
Drop-Seq
InDrop
10x
DroNc-Seq
Combinatorial indexing
sci-RNA-seq
SPLiT-seq
F.Tang 2009
SCRB-seq
Template-Switch Based
PCR amplification of “full length” cDNA
STRT-seq
SmartSeq
SmartSeq2
sNuc-Seq
Div-Seq
T7-based
Linear amplification of cDNA
CEL-seq
CEL-seq2
MARS-seq
BAT-seq
Nanowells
Seq-Well
STRT-seq-2i
Microwell-seq
Some scRNA methods

## Slide 5
Plate format
FACS (cells + nuclei) directly in lysis buffer.
Accurate (96+384 plates), if good prep low doublets assumed.
Enrich for specific populations with known markers.
Mouth pipetting under microscope for very precious samples (e.g. early embryos).
Accurate, even if doublets can be hard to discard.
Low throughput + time consuming + skills.
Combination with Patch-clamp for neurons.
Laser Capture Microdissection.
Plates with isolated single cells can be stored at -80C in lysis buffer.
Droplet-based
Cells / Nuclei are encapsulated in oil droplets using microfluidics devices.
Capture rate: Drop-seq: low | InDrop: very high with optimisations | 10x ~50%
Doublets rate can be relatively high: 1-5%.
can be used with fixed cells (although lack of all-rounder protocol)
Accurate and reproducible cell count.
Procedure between SC isolation and lysis is longer than plate format. Cell death +++
General considerations on starting material, plate vs droplets

## Slide 6
Template-Switch Based
PCR amplification of “full length” cDNA
STRT-seq
SmartSeq
SmartSeq2
SCRB-seq
sNuc-Seq
Div-Seq
Drop-Seq
T7-based
Linear amplification of cDNA
CEL-seq
CEL-seq2
MARS-seq
InDrop
10x
Combinatorial indexing
sci-RNA-seq
SPLiT-seq
DroNc-Seq
MATQ-seq
Nanowells
Seq-Well
STRT-seq-2i

## Slide 7
Template-Switch Based approaches with plate format: SmartSeq2
AAAAAAAA
TTTTTTTT-(PCR)
Cell Lysis and Poly-A capture
Single tube
CCC
(PCR)-GGG
AAAAAAAA
TTTTTTTT-(PCR)
RT + Template-Switch
AAAAAAAA-(PCR)
PCR preamplification using (PCR)
18-22cycles depending on cell type
TTTTTTTT-(PCR)
(PCR)-CCC
(PCR)-GGG
(PCR)-
Purification
“intact” mRNA
degraded mRNA
Picelli et al. Nat. Methods 2013

## Slide 8
Single tube
Purification
Illumina library preparation using Tagmentation
P5
P7
i5
i7
AAAAAAAA-(PCR)
TTTTTTTT-(PCR)
(PCR)-CCC
(PCR)-GGG
Picelli et al. Nat. Methods 2013
AAAAAAAA
TTTTTTTT-(PCR)
Cell Lysis and Poly-A capture
CCC
(PCR)-GGG
AAAAAAAA-(PCR)
TTTTTTTT-(PCR)
RT + Template-Switch
AAAAAAAA-(PCR)
PCR preamplification using (PCR)
18-22cycles depending on cell type
TTTTTTTT-(PCR)
(PCR)-CCC
(PCR)-GGG
(PCR)-
Tn5
Tn5
Tn5
Template-Switch Based approaches with plate format: SmartSeq2

## Slide 9
Template-Switch Based approaches: SmartSeq2 / STRT-Seq / SCRB-Seq
AAAAAAAA
TTTTTTTT-(PCR)
CCC
(PCR)—(UMIs)GGG
STRT-Seq
SCRB-Seq
SmartSeq2
AAAAAAAA
TTTTTTTT-(PCR)
CCC
(PCR)-GGG
AAAAAAAA
TTTTTTTT-(UMIs)-(BC)-(PCR)
CCC
(PCR)-GGG
SmartSeq2: full length / no UMIs / ~400+ cells per week
STRT-Seq: 5’ sequencing / UMIs / ~400+ cells per week
SCRB-Seq: 3’ sequencing / UMIs / ~3,000+ cells per week
Islam et al. Genome Research 2011 | Soumillon et al. bioRxiv 2014 | Bagnoli et al. Nat Commun. 2018

## Slide 10
Template-Switch Based
PCR amplification of “full length” cDNA
STRT-seq
SmartSeq
SmartSeq2
SCRB-seq
sNuc-Seq
Div-Seq
Drop-Seq
T7-based
Linear amplification of cDNA
CEL-seq
CEL-seq2
MARS-seq
InDrop
10x
Combinatorial indexing
sci-RNA-seq
SPLiT-seq
DroNc-Seq
MATQ-seq
Nanowells
Seq-Well
STRT-seq-2i

## Slide 11
T7 Based approaches – Plate format: CEL-Seq2
AAAAAAAA
TTTTTTTT-BC1-UMI-P5-T7
AAAAAAAA
TTTTTTTT-BC2-UMI-P5-T7
AAAAAAAA
TTTTTTTT-BCn-UMI-P5-T7
Cell 1
Cell 2
Cell n
AAAAAAAA
TTTTTTTT-BCn-UMI-P5-T7
RT
2d strand synthesis
TTTTTTTT-BCn-UMI-P5-T7
AAAAAAAA-BCn-UMI-P5-T7
T7 ivt - Linear amplification
Pool all cells
+ cDNA purification
TTTTTTTT-BCn-UMI-P5-T7
AAAAAAAA-BCn-UMI-P5-T7
BCn-UMI-P5
BCn-UMI-P5
BCn-UMI-P5
RT with
Integration of
Illumina “P7”
P7-NNNNNN
BCn-UMI-P5
RNA purification
PCR and indexing
P5
P7
i7
UMI-BC
Hashimshony et al. Genome Biology 2016

## Slide 12
Pros & Cons of Template-Switch versus T7 – Plate format.
SMART-Seq2
Pros: Fast, easy and reliable. Single tube until preamp: safe for precious samples.
Cons: mRNA capture depends on poly-A capture and Template-switch efficiency.
cDNA PCR amplification -> bias (+ no UMIs for SmartSeq2)
CEL-Seq2
Pros: cDNA Linear Amplification. mRNA capture depends only on poly-A.
Cons: More complex protocol.
Pooling and purification of samples before amplification -> potential loss of material
-> higher throughput
-> Both approaches are valid. Key is mRNA capture and RT efficiency. Rest is less “crucial”
Ziegenhain et al.
Mol. Cell 2017

## Slide 13
Cost SmartSeq2: ~6-7CHF per cell with sequencing
Pros & Cons of Template-Switch versus T7 – Plate format.
SMART-Seq2
Pros: Fast, easy and reliable. Single tube until preamp: safe for precious samples.
Cons: mRNA capture depends on poly-A capture and Template-switch efficiency.
cDNA PCR amplification -> bias (+ no UMIs for SmartSeq2)
CEL-Seq2
Pros: cDNA Linear Amplification. mRNA capture depends only on poly-A.
Cons: More complex protocol.
Pooling and purification of samples before amplification -> potential loss of material
-> higher throughput

## Slide 14
Template-Switch Based
PCR amplification of “full length” cDNA
STRT-seq
SmartSeq
SmartSeq2
SCRB-seq
sNuc-Seq
Div-Seq
C1
Drop-Seq
T7-based
Linear amplification of cDNA
CEL-seq
CEL-seq2
MARS-seq
InDrop
C1
10x chromium
Combinatorial indexing
sci-RNA-seq
SPLiT-seq
DroNc-Seq
MATQ-seq
Nanowells
Seq-Well
STRT-seq-2i

## Slide 15
cDNA amplification
and
library preparation
RT in beads
with template-switch
Full length cDNA amplification
Fragmentation and
Library preparation (3’)
Sequencing
R1: Barcodes + UMIs
R2: cDNA (3’ end)
10x Chromium
Gel beads + RT in droplets + template-switch approach

## Slide 16
Pros: Ready-to-use box + kits.
Instrument “cheap”.
High quality data (although lower quality than SmartSeq2).
Good cell capture rate (~50%)
Reproducibility across labs / projects +++ (unlike Drop-seq / InDrop).
Very High Throughput. If money is not an issue: 150K+ cells in 2 days (without sequencing)
Cons: Not so convenient / cost effective for low cells numbers.
Cells have to be used fresh (although cell fixation is possible – cell type…).
Price per cell is low but experiments are very expensive…
Cell counting needs to be accurate and reproducible (new cell types can be challenging).
Doublets can be an issue.
Cost SmartSeq2: ~6-7CHF per cell with sequencing.
Cost 10x genomics: ~0.5-2CHF per cell with sequencing.
Plate / 10x cut-off is ~300cells with SmartSeq2 / ~600-800cells with SCRB-seq
10x Chromium
Gel beads + RT in droplets + template-switch approach

## Slide 17
CellRanger QCplots Troubleshooting
Typical Profile
Lysis / Wetting Failure
Ambient RNA +++
-> cell death
Clogs
10x Chromium
Gel beads + RT in droplets + template-switch approach

## Slide 18
Template-Switch Based
PCR amplification of “full length” cDNA
STRT-seq
SmartSeq
SmartSeq2
SCRB-seq
sNuc-Seq
Div-Seq
C1
Drop-Seq
T7-based
Linear amplification of cDNA
CEL-seq
CEL-seq2
MARS-seq
InDrop
C1
10x chromium
Combinatorial indexing
sci-RNA-seq
SPLiT-seq
DroNc-Seq
MATQ-seq
Nanowells
Seq-Well
STRT-seq-2i
Microwell-seq

## Slide 19
Nanowells: e.g. Seq-well
Gierahn et al. Nature Methods 2017
Han et al. Cell 2018. “Mapping the Mouse Cell Atlas by Microwell-Seq”
-> 400K cells from 51 mouse tissues…

## Slide 20
Template-Switch Based
PCR amplification of “full length” cDNA
STRT-seq
SmartSeq
SmartSeq2
SCRB-seq
sNuc-Seq
Div-Seq
C1
Drop-Seq
T7-based
Linear amplification of cDNA
CEL-seq
CEL-seq2
MARS-seq
InDrop
C1
10x chromium
Combinatorial indexing
sci-RNA-seq
SPLiT-seq
DroNc-Seq
MATQ-seq
Nanowells
Seq-Well
STRT-seq-2i

## Slide 21
Combinatorial Indexing Approaches
isolated cells
/ nuclei
1000s
per well
10s
per well
first barcode
(in-situ)
second barcode
barcodes combination
gives single cell resolution
Shendure & Trapnell labs …..
Getting large number of cells without single cell compartimentalisation, only basic labware
General CONS: a lot of cells are needed.
doublets = barcodes collision can be an issue (5-10%)

## Slide 22
scRNA-seq using combinatorial indexing approaches:
sci-RNA-seq
~4500 genes per mouse cell (3T3) (~similar to 10x)
Cao 2017: can process 10,000s per experiments
Cao 2019: sci-RNAv3: 2M cells in one experiment (3 rounds of barcoding)
Cao et al. Science 2017
Pros: - do not require expensive / complicated microfluidics instruments.
- compatible with cells and nuclei. Need fixation so storage +++
Cons: a lot of cells are required.
SPLiT-seq: Rosenberg et al. Science 2018 (100K cells)

## Slide 23
Not only mRNA.
gDNA
Small RNA
ATAC-seq
BS-seq (DNA methylation)
ChIP-seq
scHiC
…
Kelsey et al. Science 2018

## Slide 24
Single Cell Chromatin Accessibility (scATAC-seq)
Pool and Split
sci-ATAC-seq
Cusanovich et al. Science 2015
coverage of 0.3-3% of DHS sites
Cusanovich et al. Cell 2018
100K cells profiled, 10-25K unique reads per cell (40% in bulk ATAC peaks)
CONS: sparse data + high doublets rate (5-10%)
10X scATAC-seq
25-35K unique reads per cell (?)
Tn5

## Slide 25
scChIP-seq
CoBATCH
Wang et al. Mol Cell 2019
targeted tagmentation
Ab
ProtA
Tn5
~10K unique reads per cell (H3K27ac)
Y
scChIP-seq
-> custom microfluidics
-> barcoded nucleosomes + “bulk” ChIP
10K unique reads per cell / loci (K27me3)
Grosselin, K. et al. Nat Genet 2019
works on single cells and single embryos

## Slide 26
DNA methylation
scBS-seq (PBAT based)
methylated and unmethylated CpGs are ”encoded” in reads

## Slide 27
PROS: 15-25% of CpGs covered (up to 40%)
CONS: relative low throughput (1,000s cells)
high cost library prep + sequencing
Smallwood et al. Nat Methods 2014
See also Farlik et al. Cell Reports 2015, Luo et al. Science 2017
scBS-seq (PBAT based)
DNA methylation

## Slide 28
Reconstructing full methylome from very low cell numbers
Smallwood et al. Nat Methods 2014
See also Farlik et al. Cell Reports 2015, Luo et al. Science 2017
scBS-seq (PBAT based)
DNA methylation

## Slide 29
Investigating DNA methylation heterogeneity
Smallwood et al. Nat Methods 2014
See also Farlik et al. Cell Reports 2015, Luo et al. Science 2017
scBS-seq (PBAT based)
DNA methylation

## Slide 30
PROs: 20-25% of CpGs covered (up to 40%)
CONs: relative low throughput (1000s cells)
high cost library prep + sequencing
sci-MET
Up to 7% of CpGs (1% median)
average throughput (~500cells)
Mulqueen et al. Nat Biotech 2018
Smallwood et al. Nat Methods 2014
See also Farlik et al. Cell Reports 2015, Luo et al. Science 2017
scBS-seq (PBAT based)
DNA methylation

## Slide 31
INTEGRATED MULTI-OMICS:
transcriptome + another layer of information from the same cell

## Slide 32
scG&T-seq: Transcriptome + Genome
scM&T-seq: Transcriptome and DNA methylome
Pros: Quality is high (5000-6000 genes + 20% of the DNA methylome)
Cons: Relative Low-Throughput + Expensive
gDNA sequencing
scBS-Seq
scG&T: Macaulay et al. Nat. Methods 2015
scM&T: Angermueller et al. Nat. Methods 2016

## Slide 33
scNMT: transcriptome + DNA methylation + chromatin accessibility
NOME-seq
Clark et al. Nat Communication 2018
~75% of promoters, ~60% of enhancers
are captured in a typical cell

## Slide 34
the epigenetic landscape of ectodermal cells is already established in the early epiblast.
regulatory elements associated with each germ layer are either epigenetically primed or epigenetically remodeled prior to overt cell fate decisions during gastrulation.
Argelaguet et al. Nature (in press + BioRXiv)
scNMT: transcriptome + DNA methylation + chromatin accessibility

## Slide 35
sci-CAR: Chromatin Accessibility + RNA
Cao et al. Science 2018
See Chen et al. Nat Biotech 2019: SNARE-seq

## Slide 36
CITE-seq / REAP-seq: cell surface markers + transcriptome
Stoeckius et al. Nat. Methods 2017
Peterson et al. Nat Biotechnology 2017
Cell hashing: increase cell loading + detection of doublets…
Stoeckius et al. Genome Biology 2018

## Slide 37
10x ”feature barcoding”
CITE-seq
CRISPR mediated perturbations to analyze regulatory gene networks and pathways
CRISPR screening (Pertub-seq)
Dixit et al. Cell 2016, Adamson et al. Cell 2016

## Slide 38
Sébastien Smallwood – FMI
sebastien.smallwood@fmi.ch
Thanks for listening…...

## Slide 39
Drop-seq: Template-switch Based
Drop-seq
barcodes
Macosko et al. Cell 2015

## Slide 40
InDrop: T7-based
Klein et al. Cell 2015

## Slide 41
Drop-seq versus InDrop
Drop-seq:
Pros: Widely adopted as beads barcodes / chips commercially available.
Cons: RT outside droplets - issue with ”ambient” RNA (cells BC with low UMIs)
High variability between set-ups…good and bad datasets out-there...
Capture rate low.
InDrop:
Pros: Quality is better than Drop-seq
Gel beads + RT within droplets (higher sensitivity).
High capture rate.
Cons: Challenging to make gel beads and barcodes (robotics helpful).
Microfluidics chips to be “made” (2 types of chips)
Now InDrop commercial solutions available